SECTION 08120

TITLE: Aluminum Doors & Frames

Aluminum Frame Glass Doors

Display hidden notes to specifier by using “Preferences”/"Tools"/"Options"/"View"/"Hidden Text".

Element Designs Inc. – Custom& functional aluminum frame glass products

This section is based on products by Element Designs, which is located at:

235 Crompton Street

Charlotte, NC 28732

Toll Free: 877-32203396

Phone: 704-332-3114

Fax: 704-332-3267

Web: www.element-designs.com

E-mail: info@element-designs.com
 
Element Designs is the leading manufacturer of aluminum frame glass cabinet doors & illuminated aluminum frame LED panels.  All products are custom manufactured to the specifier's requirements.  Element Designs’ manufacturing plant is in Charlotte, NC and ships product throughout North America through a network of 100 dependable distributors.

- GENERAL

  - SECTION INCLUDES

    - Aluminum Frame Glass Doors

  - RELATED SECTIONS

- NOTE TO SPECIFIER* Delete any sections below not relevant to this project; add others as required

A. Section 06410 – Custom Cabinets

B. Section 08810 – Glass

C. Section 12320 – Manufactured Wood Casework

D. Section 12350 – Specialty Casework

  - SUBMITTALS

    - Submit under provisions of Section 01300

    - Manufacturer’s data sheets on product being used, including: Aluminum Fame Cabinet Doors, Drawer Fronts, and Sliding Doors.

1.  Technical Manual

  - QUALITY ASSURANCE

A.    Installer Qualifications: Cabinet/Millwork Professional

  - DELIVERY, STORAGE, AND HANDLING

    - Store products in manufacturer’s unopened packaging until ready for installation.

    - Store in dry, protected, well ventilated area and protect from damage.

  - PROJECT CONDITIONS

A. 	Maintain environmental conditional (temperature, humidity, and ventilation) within limits recommended by 	manufacturer for optimal results.  Do not install products under environmental conditions outside manufacturer’s 	absolute limits.

  - WARRANTY

    - Provide manufacturer’s limited lifetime warranty

- PRODUCTS

  - MANUFACTURERS

A.  	Acceptable Manufacturer: Element Designs Inc., which is located at: 235 Crompton Street / PO Box 7747; 			Charlotte, NC 28273 / 28241; Toll Free Tel: 877-332-3396; Tel: 704-332-3114; Fax: 704-332-3267; Email: 			info@element-designs.com; Web: www.element-designs.com

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

B.	Substitutions:  Not permitted.

C.	Requests for substitutions will be considered in accordance with provisions of Section 01600.

  - Aluminum Frame Glass Doors

A. 	Approved Product: Element Designs’ AF Series Cabinetry Doors

1.  Aluminum Door Profiles:

** NOTE TO SPECIFIER **  Delete the aluminum frame profile not required in project

a. AF001 Narrow Frame 19mm (¾”) x 20.5mm (13/16”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat.

b. AF002 Wide Frame with Glass Overlay: 54mm (2 1/8”) x 20.5mm (1316”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat.

c. AF003 Wide Frame with Flat Face: 54mm (2 1/8”) x 20.5mm (1316”) profile available in natural aluminum, brushed stainless steel look, chrome look, arctic gold, black powdercoat, white powdercoat or oil rubbed bronze powdercoat.

d. AF004 Wide Frame with Glass Overlay: 45mm (1 3/4”) x 20.5mm (1316”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat.

e. AF005 Wide Frame with Radius Face: 45mm (1 3/4”) x 20.5mm (1316”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat.

f. AF006 Wide Frame with Minimal Aluminum Lip Exposed: 54mm (2 1/8”) x 20.5mm (13/16”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat. (ONLY available with opaque backpainted glass inserts, permanently adhered to frame)

g. AF007 Wide Frame with Flat Face: 70mm (2 3/4”) x 20.5mm (13/16”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat.

h. AF008 Narrow Frame with Glass Overlay 19mm (¾”) x 20.5mm (13/16”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat.

i. AF009 Wide Frame with Flat Face: 63.5mm (2 1/2”) x 16.5mm (21/32”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat (For use with 6mm or 1/4” inserts).

j. AF010 Wide Frame with Flat Face: 54mm (2 1/8”) x 20.5mm (13/16”) profile available in natural aluminum, brushed stainless steel look, chrome look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat (ONLY available with opaque backpainted glass inserts, permanently adhered to frame)

j. AF011 Wide Frame with Flat Face: 57.2mm (2 1/4”) x 19mm (3/4”) profile available in natural aluminum, brushed stainless steel look, black powdercoat, white powdercoat or oil rubbed bronze powdercoat

- Standard Insert Options:

** NOTE TO SPECIFIER **  Delete the standard glass option not required in project OR complete section if other insert type specified

a. 4mm (5/32”) tempered safety Satin (acid etched) glass – Class 3 (maximum etching) translucency

b. 4mm (5/32”) tempered safety Reeded glass with ¼” spacing between pattern

c. 4mm (5/32”) tempered safety Clear glass

d. 4mm (5/32”) tempered safety Listral D glass

e. 4mm (5/32”) tempered safety Master Carre glass

f. 4mm (5/32”) tempered safety Low Iron Clear glass

g. 4mm (5/32”) tempered safety Low Iron Satin (acid etched) glass

h. 4mm (5/32”) tempered safety Smoked Grey glass

i. 4mm (5/32”) un-tempered Mirror glass with safety laminate backer

j. 6mm (1/4”) tempered Reflective Bronze glass

- Backpainted Glass Insert Options (high quality water based coating designed for glass adhesion):

** NOTE TO SPECIFIER **  Delete the Backpainted Glass option not required in project OR complete section if other insert type specified

a. 4mm (5/32”) tempered safety White Gloss backpainted glass

b. 4mm (5/32”) tempered safety White Matte backpainted glass

c. 4mm (5/32”) tempered safety Black Gloss backpainted glass

d. 4mm (5/32”) tempered safety Black Matte backpainted glass

e. 4mm (5/32”) tempered safety Charcoal Gloss backpainted glass

f. 4mm (5/32”) tempered safety Charcoal Matte backpainted glass

g. 4mm (5/32”) tempered safety Sand Gloss backpainted glass

h. 4mm (5/32”) tempered safety Sand Matte backpainted glass

i. 4mm (5/32”) tempered safety Olive Gloss backpainted glass

j. 4mm (5/32”) tempered safety Olive Matte backpainted glass

k. 4mm (5/32”) tempered safety Mocha Gloss backpainted glass

l. 4mm (5/32”) tempered safety Mocha Matte backpainted glass

m. 4mm (5/32”) tempered safety Scarlet Gloss backpainted glass

n. 4mm (5/32”) tempered safety Scarlet Matte backpainted glass

o. 4mm (5/32”) tempered safety Silver Metallic Gloss backpainted glass

p. 4mm (5/32”) tempered safety Silver Metallic Matte backpainted glass

q. 4mm (5/32”) tempered safety Bronze Metallic Gloss backpainted glass

r. 4mm (5/32”) tempered safety Bronze Metallic Matte backpainted glass

s. 4mm (5/32”) tempered safety Non-Standard Color glass (selection of 277 pre-formulated RAL colors– see Element Designs’ website or catalog)

t. 4mm (5/32”) tempered safety Custom Color glass (Element Designs can match any paint supplier’s SOLID color code or by a physical color swatch.  Color samples on specified glass finish will be produced and approved prior to production.)

4. PARAPAN® Inserts by Evonik Industries

** NOTE TO SPECIFIER **  Delete the PARAPAN Insert  not required in project OR complete section if other insert type specified

a. 4mm (5/32”) PARAPAN high gloss solid surface insert 5910 – Alpine White

b. 4mm (5/32”) PARAPAN high gloss solid surface insert 5907 –  White

c. 4mm (5/32”) PARAPAN high gloss solid surface insert 5196 – Opal White

d. 4mm (5/32”) PARAPAN high gloss solid surface insert 5772 – Latte

e. 4mm (5/32”) PARAPAN high gloss solid surface insert 5525 –  Pale Ivory

f. 4mm (5/32”) PARAPAN high gloss solid surface insert 5421 - Mint

g. 4mm (5/32”) PARAPAN high gloss solid surface insert 5773 – Cappuccino

h. 4mm (5/32”) PARAPAN high gloss solid surface insert 5570 –  Orange

i. 4mm (5/32”) PARAPAN high gloss solid surface insert 5771 – Oxide Red

j. 4mm (5/32”) PARAPAN high gloss solid surface insert 5655 –  Signal Red

k. 4mm (5/32”) PARAPAN high gloss solid surface insert 5380 – Cobalt Blue

l. 4mm (5/32”) PARAPAN high gloss solid surface insert 5440 – Kiwi

m. 4mm (5/32”) PARAPAN high gloss solid surface insert 5776 –  Brown

n. 4mm (5/32”) PARAPAN high gloss solid surface insert 5299 – Black

o. 4mm (5/32”)  PARAPAN high gloss solid surface insert 5295 – Stone Grey

p. 4mm (5/32”)  PARAPAN high gloss solid surface insert 5290 –  Light Grey

q. 4mm (5/32”)  PARAPAN high gloss solid surface insert 5471 – Turquoise

r. 4mm (5/32”)  PARAPAN high gloss solid surface insert 5600 – Bordeaux

5.  Architectural Resin Inserts by 3Form:

** NOTE TO SPECIFIER **  Delete the Architectural Resin not required in project OR complete section if other insert type specified

a. 4mm (5/32”) Thatch architectural resin insert

b. 4mm (5/32”) Bear Grass architectural resin insert

c. 4mm (5/32”) Fossil Leaves architectural resin insert

d. 4mm (5/32”) Linea Ivory architectural resin insert

e. 4mm (5/32”) Wisp Silver architectural resin insert

f. 4mm (5/32”) Quattro Carbon architectural resin insert

g. 4mm (5/32”) Ting Ting architectural resin insert

h. 4mm (5/32” Pop Clear architectural resin insert

- Metallic Insert Options

** NOTE TO SPECIFIER **  Delete the Metallic Insert  not required in project OR complete section if other insert type specified

  - 4mm (5/32”) anodized aluminum insert panel

  - 4mm (5/32”) brushed stainless look aluminum insert panel

  - 4mm (5/32”) platinum ice acrylic

7.  Leather Insert Options:

** NOTE TO SPECIFIER **  Delete the Architectural Resin not required in project OR complete section if other insert type specified

a. 4mm (5/32”) Antique Brown Walrus leather insert

b. 4mm (5/32”) Coal Buffalo leather insert

c. 4mm (5/32”) Grey Thunder Buffalo leather insert

d. 4mm (5/32”) Bianco Jumbo Croc leather insert

PART 3   	 EXECUTION

  - EXAMINATION

A. 	Do not begin installation until all products are properly prepared and hardware installed.

3.2      INSTALLATION

A.	 Install in accordance to manufacturer’s instructions using screw on European concealed hinges.

3.3	PROTECTION

A. 	 Protect installed product until completion of project.

END OF SECTION